c h g r o o t                                     s.a 2.9.92

        CHGROOT is a DOS program to change the root device in a Linux boot
        image - the two bytes at offset 508 and 509. The image can be either
        a DOS disk file or a boot diskette written with RAWRITE or 'dd'.
        If you have a disk editor and remember Linux major and minor
        numbers, you won't need this program.



        u s e

        The command line is

             chgroot filename | -a | -b

        Use <filename> if the bootimage is in a DOS file, say
        E:LINUX\BOOT0971.IMG.
        Use -a or -b if the bootimage is a floppy in drive A: or B:.

        CHGROOT displays the current root device and prompts you for a new
        one. If you input a device that the program recognizes, CHGROOT
        updates the file/floppy.

        The devices recognized are
            0           (root device=boot device)
            fd0,fd1
            hda1..hda8, hdb1..hdb8
            sda1..8, sdb1..8
        If CHGROOT doesn't find one of these in the alleged bootimage,
        it will complain and die.



        c a v e a t

        I took the major/minor numbers from root diskette 0.97.



        b u g   r e p o r t s

        sakaria@vipunen.hut.fi